## Slide 1: THE Saint-Gobain GROUP
MARCH 2022

## Slide 2: SEAMLESS ACOUSTIC CEILING SYSTEM

## Slide 3: Product to system solution

## Slide 4: Installation of Ecophon fade seamless acoustic ceiling system
Below detail is for understanding purpose only
25 & 40mm Saint-Gobain E Acoustic Panel
Saint-Gobain
Fade Acoustic Plaster
0.8 & 0.9NRC
MF Seamless Sound Acoustic solution

## Slide 5: Integration with other ceiling solutions
120mins Fire Rated
60mins Fire Rated
Framing Thickness & Framing Distance Vary based on load
Mass Barrier
GAH Acoustic Hanger
Below details are for understanding purpose only
When combined with Fire Rated & other MF ceiling assembly, the performance of it too can be added to the attributes.
Curve

## Slide 6: Sound absorption performance of Ecophon fade
ULTRA SMOOTH FINISH
25mm Thick : 0.80 NRC | 0.85 αw
SMOOTH FINISH
40mm Thick : 0.90 NRC | 0.90 αw
40mm Thick : 1.0 NRC | 0.95 αw 40mm Thick : 1.0 NRC | 1.0 αw

## Slide 7: Sound insulation performance using mf gypsum ceiling
Detail | Air Cavity | Board Type | Board Thickness | Insulation | Sound Insulation between floor Rw ¦ Lnw | CAC Rw ¦ STC (Based on partition assembly) | Sound Insulation between MEP to ceiling Rw ¦ STC (Based on software prediction)
1 | 240mm | Saint-Gobain Fire Rated | 1x12.5mm | N/A | 56dB ¦ 68dB | 39dB ¦ 41dB | 28dB ¦ 27dB
2 | 240mm | Saint-Gobain Fire Rated | 2x12.5mm | N/A | 60dB ¦ 64dB | 46dB ¦ 47dB | 34dB ¦ 33dB
3 | 240mm | Saint-Gobain Fire Rated | 1x12.5mm | 100mm (16Kg/m3) | 61dB ¦ 60dB | 44dB ¦ 44dB | 31dB ¦ 31dB
4 | 240mm | Saint-Gobain Fire Rated | 2x12.5mm | 100mm (16Kg/m3) | 64dB ¦ 57dB | 53dB ¦ 53dB | 37dB ¦ 37dB
5 | 240mm | Saint-Gobain Fire Rated | 3x15.9mm | 50mm (50Kg/m3) | 64dB ¦ 57dB | 53dB ¦ 53dB | 47dB ¦ 47dB
MF Ceiling installed below to 150mm Thick Concrete slab with air cavity of 240mm.
5

## Slide 8: Offers all in one acoustic solution
All above are laboratory Test measurement
LnTw
Sound transferred through Ceiling
Sound Transmission Class (STC) measured in dB

## Slide 9: Ecophon fade seamless acoustic ceiling installation video
Fixation detail below Saint-Gobain MF Ceiling Assembly

## Slide 10: Ecophon fade seamless acoustic ceiling maintenance & repair video
Excellent Spot Repair feasibility

## Slide 11: Special effects options
Sky Effect
Timber/wood Effect
Marble Effect
Other Effects

## Slide 12: Finishing images from site
Cut out for Access Panel
Finishing under progress

## Slide 13: Integration with Saint-Gobain Gyproc access panel

## Slide 14: Finishing images

## Slide 15: Site support & training activity

## Slide 16: Few Reference projects
Hankook Tire HQ
The Eiffel Tower – Le Jules Verne
Helsinki Olympic Stadium
European Chemicals Agency
Niittykumpu Metro Station
Wadden Sea Centre
Holmens Kanal 9
Museum of the Future
Dubai Mall
Royal Atlantis
Juma Mosque – Qeitaifan island

## Slide 17: THANK YOU